MAG VEST APPLICATION INSTRUCTIONS

(For models 695SHBD, 695SHV, 695SH4, and SHV Option)

DESCRIPTION :

695SHBD – A suspension vest for assisted walking, unweighting therapy, gait training, stroke and spinal chord rehabilitation. The vest uses a patented “Chinese Finger Trap” methodology, which grips the torso when upward force is applied to the adjustable length, one-piece shoulder straps preventing, along with the leg straps, the vest from sliding up.

Crotch strap not shown

695SHV – Same as above but with a single belt crotch strap in lieu of leg straps.

695SH4 – Same as the 695SHBD but with four independently adjustable should straps provided with carabiners to join the straps together and allow attachment to the spreader bar.

SHV Option – The single belt crotch strap added to the 695SHBD or 695SH4 to accompany the leg straps.

APPLICATION:

Crotch strap not shown

- Open vest and unhook all Velcro attachments. Leg wraps can be left “as is” until the vest is fitted.

- Put arms through shoulder straps and put on vest, open side towards the front.

- Attach lower abdominal support first.  Side elastic straps on the lower abdominal support should be loose. For best results, lower abdominal support should be as tight as possible.

- Attach middle, netting, Velcro attachment next.

- Attach top strap (chest) by looping it through the cinch loop and connecting it back onto itself.

- Tighten elastic side straps on lower abdominal support.

- Adjust one-inch vertical straps. These straps are intended to keep garment shorter on the torso if necessary.

- Apply the leg straps, or crotch strap, or both, if provided. Simply wrap the neoprene leg wraps around the upper thigh. Tighten the straps that connect the wraps to the garment to prevent the vest from sliding into the axilla (arm pits).

- Adjust shoulder straps (2 or 4, depending on model) to desired length.